## Slide 1
GOM file user guide

## Slide 2: Dimension, element type and formulation
### Anura3D_2022 ###
$$DIMENSION
3D-cartesian
3D-cylindrical
2D-plane_strain
2D-axisymmetric
$$ELEMENTTYPE
tetrahedral_old
triangular_3-noded
$$FORMULATION
single-point
double-point
3D models
2D models

## Slide 3: Mesh data
$$STARTCOUNTERS
Number of elements Number of nodes
0 0
$$STARTNODES
Nodal coordinate x Nodal coordinate y Nodal coordinate z (3D only)
0 0 0
…
$$STARTELEMCON
3D models
Nodes ID of each element (10 for 3D)
0 0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each element (3 for 2D)
0 0 0
…

## Slide 4: Solid fixities
$$START_FIXITY_SURFACE_SOLID
Number of nodes belonged to surfaces on which solid fixity is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_FIXITY_LINE_SOLID
Number of nodes belonged to lines on which solid fixity is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_FIXITY_POINT_SOLID
Number of nodes belonged to points on which solid fixity is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…

## Slide 5: Liquid fixities
$$START_FIXITY_SURFACE_LIQUID
Number of nodes belonged to surfaces on which liquid fixity is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_FIXITY_LINE_LIQUID
Number of nodes belonged to lines on which liquid fixity is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_FIXITY_POINT_LIQUID
Number of nodes belonged to points on which liquid fixity is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0 0/1
…

## Slide 6: Gas fixities
$$START_FIXITY_SURFACE_GAS
Number of nodes belonged to surfaces on which gas fixity is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_FIXITY_LINE_GAS
Number of nodes belonged to lines on which gas fixity is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_FIXITY_POINT_GAS
Number of nodes belonged to points on which gas fixity is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…

## Slide 7: Removing solid fixities
$$START_REMOVE_FIXITY_SURFACE_SOLID
Number of nodes belonged to surfaces on which solid fixity removal is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_REMOVE_FIXITY_LINE_SOLID
Number of nodes belonged to lines on which solid fixity removal is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_REMOVE_FIXITY_POINT_SOLID
Number of nodes belonged to points on which solid fixity removal is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…

## Slide 8: Removing liquid fixities
$$START_REMOVE_FIXITY_SURFACE_LIQUID
Number of nodes belonged to surfaces on which liquid fixity removal is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_REMOVE_FIXITY_LINE_LIQUID
Number of nodes belonged to lines on which liquid fixity removal is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_REMOVE_FIXITY_POINT_LIQUID
Number of nodes belonged to points on which liquid fixity removal is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…

## Slide 9: Removing gas fixities
$$START_REMOVE_FIXITY_SURFACE_GAS
Number of nodes belonged to surfaces on which gas fixity removal is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_REMOVE_FIXITY_LINE_GAS
Number of nodes belonged to lines on which gas fixity removal is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…
$$START_REMOVE_FIXITY_POINT_GAS
Number of nodes belonged to points on which gas fixity removal is applied
0
NodeID x-direction y-direction z-direction (3D only) (0 free ; 1 fixed)
0 0/1 0/1 0/1
…

## Slide 10: Initial soil surface ( for k0- procedure)
$$START_SOIL_SURFACE_NODES
Number of elements sides belonging to lines or surfaces specified as soil surface
0
3D models
Nodes ID of each element side (6 for 3D)
0 0 0 0 0 0
…
2D models
Nodes ID of each element side (2 for 2D)
0 0
…

## Slide 11: Initial phreatic surface ( for k0- procedure)
If drawn as lines or surfaces in the geometry:
$$START_PHREATIC_SURFACE_NODES
Number of elements sides belonging to lines or surfaces specified as phreatic surface
0
3D models
Nodes ID of each element side (6 for 3D)
0 0 0 0 0 0
…
2D models
Nodes ID of each element side (2 for 2D)
0 0
…
If defined in an external .txt file:
$$INITIAL_WATER_SURFACE_FROM_FILE
Number of materials on which an initial water surface is assigned
0
Material ID .txt file path
0 C:\…
…

## Slide 12: Hydraulic boundary conditions
$$BOUNDARY_HYDRAULIC_HEAD_AREA
x-min x-max
0 0
y-min y-max
0 0
z-min z-max (3D only)
0 0
$$BOUNDARY_SEEPAGE_AREA
x-min x-max
0 0
y-min y-max
0 0
z-min z-max (3D only)
0 0

## Slide 13: Hydraulic boundary conditions
$$BOUNDARY_INFILTRATION_AREA
x-min x-max
0 0
y-min y-max
0 0
z-min z-max (3D only)
0 0
$$INFILTRATION_RATE
x-value y-value z-value (3D only)
0 0 0

## Slide 14: Loading conditions on solid: SYSTEM A
$$START_LOAD_ON_NODES_SOLID
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…
$$START_LOAD_ON_MATERIAL_POINTS_SOLID
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…

## Slide 15: Loading conditions on solid: SYSTEM B
$$START_LOAD_ON_NODES_SOLID_B
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…
$$START_LOAD_ON_MATERIAL_POINTS_SOLID_B
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…

## Slide 16: Loading conditions on liquid: SYSTEM A
$$START_LOAD_ON_NODES_LIQUID
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…
$$START_LOAD_ON_MATERIAL_POINTS_LIQUID
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…

## Slide 17: Loading conditions on liquid: SYSTEM B
$$START_LOAD_ON_NODES_LIQUID_B
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…
$$START_LOAD_ON_MATERIAL_POINTS_LIQUID_B
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…

## Slide 18: Loading conditions on gas: SYSTEM A
$$START_LOAD_ON_NODES_GAS
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…
$$START_LOAD_ON_MATERIAL_POINTS_GAS
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…

## Slide 19: Loading conditions on gas: SYSTEM B
$$START_LOAD_ON_NODES_GAS_B
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…
$$START_LOAD_ON_MATERIAL_POINTS_GAS_B
Number of loaded element sides
0
3D models
Nodes ID of each loaded element side (6 for 3D) x-value(1) y-value(1) z-value(1)…
0 0 0 0 0 0 0 0 0
…
2D models
Nodes ID of each loaded element side (2 for 2D) x-value(1) y-value(1)…
0 0 0 0
…

## Slide 20: Prescribed velocity on MPs
$$PRESCRIBED_MATERIAL_POINT_VELOCITY_VOLUME
Number of elements
0
Element ID x-direction y-direction z-direction (3D only) x-value y-value z-value (3D only)
0 0/1 0/1 0/1 0 0 0
…
$$PRESCRIBED_MATERIAL_POINT_VELOCITY_SURFACE
Number of elements
0
Element ID x-direction y-direction z-direction (3D only) x-value y-value z-value (3D only)
0 0/1 0/1 0/1 0 0 0
…

## Slide 21: Prescribed velocity on nodes
$$PRESCRIBED_NODAL_VELOCITY_VOLUME
Number of nodes
0
Node ID x-direction y-direction z-direction (3D only) x-value y-value z-value (3D only)
0 0/1 0/1 0/1 0 0 0
…
$$PRESCRIBED_NODAL_VELOCITY_SURFACE
Number of nodes
0
Node ID x-direction y-direction z-direction (3D only) x-value y-value z-value (3D only)
0 0/1 0/1 0/1 0 0 0
…

## Slide 22: Prescribed velocity on nodes
$$PRESCRIBED_NODAL_VELOCITY_LINE
Number of nodes
0
Node ID x-direction y-direction z-direction (3D only) x-value y-value z-value (3D only)
0 0/1 0/1 0/1 0 0 0
…
$$PRESCRIBED_NODAL_VELOCITY_POINT
Number of nodes
0
Node ID x-direction y-direction z-direction (3D only) x-value y-value z-value (3D only)
0 0/1 0/1 0/1 0 0 0
…

## Slide 23: Initial prescribed velocity on MPs
$$INITIAL_VELOCITY_MATERIAL_POINT
Number of elements
0
Element ID x-value y-value z-value (3D only)
0 0 0 0
…

## Slide 24: Contact
$$START_CONTACT_VOLUME
Number of contact elements
0
Element ID Number of materials (up to 4) Material name(1) Friction(1) Adhesion(1) …
0 0 “…” 0 0
…
$$START_BODY_CONTACT_2D
Number of contact elements
0
Element ID Number of materials (up to 4) Material name(1) Friction(1) Adhesion(1) …
0 0 “…” 0 0
…

## Slide 25: Excavation
$$START_EXCAVATION_SOLID
3D models
Excavated volume ID Excavated elements ID
0 0
…
2D models
Excavated surface ID Excavated elements ID
0 0
…

## Slide 26: Solid absorbing boundary
$$ABSORBING_BOUNDARY_SURFACE_SOLID
Number of surfaces
0
Surface ID x-direction alpha delta y-direction alpha delta z-direction (3D only) alpha delta
0 0/1 0 0 0/1 0 0 0/1 0 0
…
$$ABSORBING_BOUNDARY_LINE_SOLID
Number of lines
0
Line ID x-direction alpha delta y-direction alpha delta z-direction (3D only) alpha delta
0 0/1 0 0 0/1 0 0 0/1 0 0
…
$$ABSORBING_BOUNDARY_POINT_SOLID
Number of points
0
Point ID x-direction alpha delta y-direction alpha delta z-direction (3D only) alpha delta
0 0/1 0 0 0/1 0 0 0/1 0 0
…

## Slide 27: Liquid absorbing boundary
$$ABSORBING_BOUNDARY_SURFACE_LIQUID
Number of surfaces
0
Surface ID x-direction alpha delta y-direction alpha delta z-direction (3D only) alpha delta
0 0/1 0 0 0/1 0 0 0/1 0 0
…
$$ABSORBING_BOUNDARY_LINE_LIQUID
Number of lines
0
Line ID x-direction alpha delta y-direction alpha delta z-direction (3D only) alpha delta
0 0/1 0 0 0/1 0 0 0/1 0 0
…
$$ABSORBING_BOUNDARY_POINT_LIQUID
Number of points
0
Point ID x-direction alpha delta y-direction alpha delta z-direction (3D only) alpha delta
0 0/1 0 0 0/1 0 0 0/1 0 0
…

## Slide 28: Gas absorbing boundary
$$ABSORBING_BOUNDARY_SURFACE_GAS
Number of surfaces
0
Surface ID x-direction alpha delta y-direction alpha delta z-direction (3D only) alpha delta
0 0/1 0 0 0/1 0 0 0/1 0 0
…
$$ABSORBING_BOUNDARY_LINE_GAS
Number of lines
0
Line ID x-direction alpha delta y-direction alpha delta z-direction (3D only) alpha delta
0 0/1 0 0 0/1 0 0 0/1 0 0
…
$$ABSORBING_BOUNDARY_POINT_GAS
Number of points
0
Point ID x-direction alpha delta y-direction alpha delta z-direction (3D only) alpha delta
0 0/1 0 0 0/1 0 0 0/1 0 0
…

## Slide 29: Moving mesh
$$EXTENDING_MESH_CORNER_NODES
Extending mesh corner nodes ID
0
…
$$COMPRESSING_MESH_CORNER_NODES
Compressing mesh corner nodes ID
0
…
$$MOVING_MESH_CORNER_NODES
Moving mesh corner nodes ID
0
…

## Slide 30: Moving mesh
$$MOVING_MESH_DIRECTION
x-direction
y-direction
z-direction
$$MOVING_MESH_REFERENCE_MATERIAL_INDEX
Reference material ID
0

## Slide 31: Reaction forces
$$START_OUTPUT_REACTION_FORCES
Number of surfaces
0
3D models
Surface identifier Element ID Boundary nodes ID (6 for 3D)
“….” 0 0 0 0 0 0 0
…
2D models
Surface identifier Element ID Boundary nodes ID (2 for 2D)
“….” 0 0 0
…

## Slide 32: Material properties
$$NUMBER_OF_MATERIALS
0
$$MATERIAL_INDEX
0
$$MATERIAL_NAME
name_of_material
$$MATERIAL_TYPE
dry_material
saturated_material_drained
saturated_material_undrained_effective
saturated_material_undrained_total
saturated_material_coupled
unsaturated_material_2phase_suction
unsaturated_material_3phase_coupled
Liquid

## Slide 33: Material types
$$MATERIAL_TYPE
dry_material
$$POROSITY_SOLID
0
$$DENSITY_SOLID
0
$$K0_VALUE_SOLID
0
2. $$MATERIAL_TYPE
saturated_material_drained
$$POROSITY_SOLID
0
$$DENSITY_SOLID
0
$$DENSITY_LIQUID
0
$$K0_VALUE_SOLID
0
3. $$MATERIAL_TYPE
saturated_material_undrained_effective
$$POROSITY_SOLID
0
$$DENSITY_SOLID
0
$$DENSITY_LIQUID
0
$$K0_VALUE_SOLID
0
4. $$MATERIAL_TYPE
saturated_material_undrained_total
$$POROSITY_SOLID
0
$$DENSITY_SOLID
0
$$DENSITY_LIQUID
0
$$K0_VALUE_SOLID
0

## Slide 34: Material types
5. $$MATERIAL_TYPE
saturated_material_coupled
$$POROSITY_SOLID
0
$$DENSITY_SOLID
0
$$DENSITY_LIQUID
0
$$INTRINSIC_PERMEABILITY_LIQUD
0
$$BULK_MODULUS_LIQUID
0
$$DYNAMIC_VISCOSITY_LIQUID
0
$$K0_VALUE_SOLID
0

## Slide 35: Material types
6. $$MATERIAL_TYPE
unsaturated_material_2phase_suction
$$POROSITY_SOLID
0
$$DENSITY_SOLID
0
$$DENSITY_LIQUID
0
$$INTRINSIC_PERMEABILITY_LIQUID
0
$$BULK_MODULUS_LIQUID
0
$$DYNAMIC_VISCOSITY_LIQUID
0
$$K0_VALUE_SOLID
0
7. $$MATERIAL_TYPE
unsaturated_material_3phase_coupled
$$POROSITY_SOLID
0
$$DENSITY_SOLID
0
$$DENSITY_LIQUID
0
$$DENSITY_GAS
0
$$INTRINSIC_PERMEABILITY_LIQUID
0
$$INTRINSIC_PERMEABILITY_GAS
0
$$BULK_MODULUS_LIQUID
0
$$BULK_MODULUS_GAS
0
$$DYNAMIC_VISCOSITY_LIQUID
0
$$DYNAMIC_VISCOSITY_GAS
0
$$K0_VALUE_SOLID
0

## Slide 36: Unsaturated material water retention curve
I. $$WATER_RETENTION_CURVE
linear
$$av
0
II. $$WATER_RETENTION_CURVE
van_genuchten
$$Smin
0
$$Smax
0
$$P0
0
$$L
0

## Slide 37: Unsaturated material hydraulic conductivity curve
I. $$HYDR_CONDUCTIVITY_CURVE
constant
II. $$HYDR_CONDUCTIVITY_CURVE
Hillel
$$r
0
III. $$HYDR_CONDUCTIVITY_CURVE
mualem
$$Smin
0
$$Smax
0
$$P0
0
$$L
0

## Slide 38: Material types
8. $$MATERIAL_TYPE
Liquid
$$DENSITY_LIQUID
0
$$BULK_MODULUS_LIQUID
0
$$DYNAMIC_VISCOSITY_LIQUID
0
$$LIQUID_CAVITATION
0
$$APPLY_DETECT_LIQUID_SURFACE
0

## Slide 39: Material model solid
1. $$MATERIAL_MODEL_SOLID
linear_elasticity
$$YOUNG_MODULUS
0
$$POISSON_RATIO
0
2. $$MATERIAL_MODEL_SOLID
mohr_coulomb
$$YOUNG_MODULUS
0
$$POISSON_RATIO
0
$$FRICTION_ANGLE
0
$$COHESION
0
$$DILATANCY_ANGLE
0
$$TENSILE_STRENGTH
0
3. $$MATERIAL_MODEL_SOLID
rigid_body
$$constraint_XDISPLACEMENT
(0 free ; 1 fixed)
0
$$constraint_YDISPLACEMENT
(0 free ; 1 fixed)
0
$$constraint_ZDISPLACEMENT
(0 free ; 1 fixed)
0

## Slide 40: Material model solid
4. $$MATERIAL_MODEL_SOLID
external_soil_model
$$MATERIAL_MODEL_DLL
specify file name without extensión
$$UMAT_DIMENSION
- full_3D_(default)
- 2D_plane_strain
$$MATERIAL_PARAMETER_SOLID_01
0.0
…
$$MATERIAL_PARAMETER_SOLID_50
0.0
$$INITIAL_STATE_VARIABLE_SOLID_01
0.0
…
$$INITIAL_STATE_VARIABLE_SOLID_50
0.0
3D models
2D models

## Slide 41: Material model liquid
1. $$MATERIAL_MODEL_LIQUID
bingham_liquid
$$BINGHAM_YIELD_STRESS
0
$$BINGHAM_YOUNG_MODULUS
0
$$BINGHAM_POISSON_RATIO
0
2. $$MATERIAL_MODEL_LIQUID
newtonian_liquid

## Slide 42: Further mesh data
$$STARTELMMAT
Material ID of each element
0
…
$$STARTDAMPING
Damping value for each element
0
…
$$START_NUMBER_OF_MATERIAL_POINTS
Number of solid MPs for each element Number of liquid MPs for each element
0 0
…